## Slide 1: Mitigating non-CO2 emissions in civil aviation
Non-CO2 aircraft emissions responsible for 2/3rds of aviation’s net climate impact.
NOx, contrails, and other factors strongly depend on atmospheric conditions, i.e. their climate impact is spatio-temporally sensitive.
Climate-optimal routing – optimising flight routes to avoid climate sensitive regions of the atmosphere.
  Potential to reduce aviation climate impact by 10-20% for only a few percent additional fuel consumption.
Formation flight – aligning flight tracks to overlap aircraft plumes
  Aerodynamic benefits – 5-8% reduction in fuel burn and CO2.
  Emissions saturation benefits (non-CO2) – reduced ozone production efficiency (~5%) and diminishing contrail effect (~15%) for follower aircraft.
Industry fixation on carbon emissions limiting progress on short term non-CO2 climate impact reduction.
Kieran Tait – PhD student supervised by: Steve Bullock, Mark Lowenberg and Dudley Shallcross (Atmospheric Chemistry).